## Slide 1: Turning a Stepper Motor with a Joystick Arduino with C Programming
ELECTRICAL ENGINEERING AND COMPUTER SCIENCE, COLLEGE OF ENGINEERING AND PHYSICAL SCIENCES
Notes: Updated 13 Jun 2024 by Noah Mulvaney

## Slide 2: Goals
Take analog values from a joystick and convert them to digital values and use them to rotate our stepper motor
Use the ULN2003 Stepper Motor Driver Module to easily attach and control the stepper motor

## Slide 3: What is a Stepper Motor?
A Stepper Motor is controlled with electromagnetic fields
The 28-BYJ48 Stepper Motor contains two coils, a magnet in the middle attached to the rotor, and ‘teeth’ on the stator of the motor
Each time the motor moves from one ‘tooth’ to another we call that a step
This Stepper Motor has 32 steps in one revolution
When sending an electric pulse to a coil we can induce a magnetic field that attracts the magnet therefore turning the rotor

## Slide 4: What is a Stepper Motor?
The ULN2003 Stepper Motor Driver Module allows us to control the stepper motor with ease
Gives us organized connections from the Arduino to the motor

## Slide 5: What is a Joystick?
A joystick is made up of two potentiometers and a pushbutton
There are two potentiometers for each axis (x and y), we will only be using the x axis potentiometer to rotate the stepper motor
A potentiometer is a variable resistor, the potentiometers in this joystick are connected between five volts and ground
When our potentiometer is at full resistance, we have a minimum value and vice versa
When pushing down the joystick you enable the pushbutton

## Slide 6: What is a Joystick?
When we move the joystick all the way in one direction, we are either reading five or zero volts
Instead of reading a value between five and zero volts to the Arduino, we need to put these numbers to a digital value (0-1023) using the built in ADC (analog-to-digital converter)
We can then use this digital value in our Arduino code in whatever way we want

## Slide 7: Circuit Diagram
Arduino Pins
  Pin 11: IN1
  Pin 10: IN2
  Pin 9: IN3
  Pin 8: IN4
  Pin A0: VRx
A0
11 10 9 8

## Slide 8: Completing the Code

## Slide 9: Completing the Code

## Slide 10: Completing the Code

## Slide 11: Completing the Code

## Slide 12: Test it Out!
Open your serial monitor and observe the values shown when moving the joystick