## Slide 1: Arduino Programming using C
Digital inputs and outputs
Analog inputs and outputs
Making decisions with ‘if’
Loops
Goal: learn enough to understand the modules and get you started on writing your own C programs

## Slide 2: digitalRead and digitalWrite
Suppose we want to turn on LED connected to pin 8
    digitalWrite(8,HIGH); //sets pin 8 to 5V
    digitalWrite(8,LOW); //sets pin 8 to 0V
Now suppose we want to read the voltage present on pin 9
    int x = digitalRead(9);
  Declares variable x to be an integer type
  Reads pin 9 voltage
  Stores either LOW or HIGH into x
    Actual values stored is either 0 or 1
Input
Output

## Slide 3: Meaning of LOW and HIGH
Suppose we want to read a digital input on pin 6
X = digitalRead(6);
  In the real world, voltages are noisy
  The actual voltage may range anywhere from below 0 V to over 5 V.
  How is this converted into a binary result?
Arduino electronics make this happen:
  If volts then X = LOW ( stored as 0)
  If volts then X = HIGH (stored as 1)
Now we can use digitalRead to sense a pushbutton!
  A small amount of noise won’t bother us
5V
No noise
0V
5V
Noisy
0V

## Slide 4: Push Button Switch
Pushing button connects left 2 pins to right 2 pins

## Slide 5: How to use a Push Button switch A difficulty:
If you push the button:
  Voltage on Pin 3: V3= 0 = LOW
If you don’t push the Button:
  V3 is not defined
  This is called a “floating input”
  Gives random results.
    Sometimes HIGH, sometimes LOW
    This is Bad.
Pin 3
Gnd
Switch
V3

## Slide 6: Solution: Use a “Pull-up” resistor
Now, if you don’t push the button:
  V is “pulled up” toward +5V (HIGH)
  It’s not quite 5V but close enough
  The input is no longer floating
If you do push the button:
  V = 0 (LOW)
Nothing is floating - Problem is solved!!!!
Pull-up Resistor R
V
Arduino pin
Gnd
Switch
+5 V
Could we just use a jumper instead of a resistor (i.e., R=0)? NO!
  Pushing the button shorts +5V to GND
  Excessive current:
  This would damage the Arduino

## Slide 7: Built-In Pull-up Resistor
Arduino has built-in pull-up resistors
  So we don’t need to put one into our circuit
They are optional. Activate using:
  pinMode(PinNumber, INPUT_PULLUP);
Just remember:
  Button pushed: digitalRead is LOW
  Button not pushed: digitalRead is HIGH

## Slide 8: Getting Help
Use Help->Reference
Click Here for all terms
or Highlight term and click here

## Slide 9: if statement
This is how computers make decisions
  E.g., is a sensor value above a certain number?
The format for an if test is:
if (someVariable > 50)
{
digitalWrite(LEDpin,HIGH);
}
if (Condition True)
{
statements
}
Example
Format

## Slide 10: if details
General form of “if statement”: if (Boolean expression) {bunch of statements}
“Boolean”means its value is true or false
Examples of Boolean expressions:
  X==Y meaning: X equals Y
  X!=Y meaning: X not equal to Y
  X>=Y meaning: X greater or equal to Y
  X==Y && W==3 meaning: “&&” is AND
  X>Y || X==5 meaning: “||” is OR

## Slide 11
Objective: Learn about IF statements
  Build simple circuit with switches and LEDs
  Experiment with different uses of “if” statement
Hands On

## Slide 12: Build This Circuit
Pin 5 – left LED
Pin 4 – left button
Pin 3 – right button
Pin 2 – right LED
Hands On

## Slide 13: Your Assignment:
Open IfExample.ino from Templates folder
Edit to look like this
Understand the sketch
Upload the program
Does it do what you think it should do?
Hands On

## Slide 14: What does “=“ mean?
In Algebra, X=Y means that X and Y have same value
  The statement X = X+1 is not meaningful
In computers X=X+1 means:
  Store the value of X+1 back into location X
  E.g., if 15 is initially stored in location X
    First compute X+1, which gives 16
    Store this value into memory location X
    Now 16 is stored in memory location X
Hands On

## Slide 15: What does “==“ mean?
Consider the C statement: if (Left== LOW) { do something}
“Left==LOW” is called a “Boolean expression”
  It is true if the value in memory location Left is LOW
  It is false otherwise
Summary
  X=Y+W; //stores the value of Y+W into variable X
  X==Y+W; //is true if the value of X equals the value Y+W //Does not store any value into X
Hands On

## Slide 16: if Statement Practice
Modify your code to accomplish following:
Right button
  When pushed, right LED is ON
  When NOT pushed, right LED is OFF
Left button
  When pushed, left LED is OFF
  When NOT pushed, left LED is ON
Hands On
Solution is in IfPractice.ino

## Slide 17: Several Forms of IF
if (x >= y) {
digitalWrite(5,HIGH);
}
if (x > y) {
digitalWrite(5,HIGH);
}
else {
digitalWrite(4,LOW);
}
if (x > y) {
digitalWrite(5,HIGH);
}
else if (x==y){
digitalWrite(4,LOW);
}
else {
digitalWrite(4,LOW);
digitalWrite(5,LOW);
}
if (x > y) {
digitalWrite(5,HIGH);
}
else if (x==y){
digitalWrite(4,LOW);
}
//no action taken if x<y
Hands On

## Slide 18: Practice Assignment
Modify your sketch to read the right button using “digitalRead(pin #);”
Then use one of the if-else statements on the previous slide to accomplish the following
When right button pressed
  The right LED will illuminate
  The left LED is off
When released (this is the “else” part)
  The left LED will illuminate
  The right LED is off
Hands On
Solution in IfElse.ino

## Slide 19: If you have time (or do at home)
Modify your sketch using two if-else if statements to do following
Condition to turn on Left LED (called an “inclusive OR”)
  If left OR right OR both buttons pressed
  Otherwise, left LED is off
Condition to turn on Right LED (called an “exclusive OR”)
  If either Left or Right button pressed (but not both)
  If both buttons pressed OR no buttons pressed, then LED is OFF (use if–else, or combine conditions into one if)
Solution is in: LastIfELseExample.ino
Hands On
Notes: There are many solutions
Suppose we start with:
int Left = digitalRead(LeftSwitch);
int Right = digitalRead(RightSwitch);
Exclusive OR can be done like this:
If (Left==LOW && Right==HIGH) digitalWrite(pin,HIGH);
Else if (Right==LOW && Left==HIGH) digitalWrite(pin,HIGH);
Or like this:
If (Left==LOW && Right==HIGH || Right==LOW&&Left==HIGH) digitalWrite(pin,HIGH);
Or simplest: if (Left != Right) digitalWrite(pin,HIGH); else digitalWrite(pin,LOW);

## Slide 20: Repeating Statements with “Loops”
While loop: Repeat a group of statements as long as condition remains true
  E.g., Turn on LED light as long as temp > 90
For loop: Repeat statements a fixed number of times
  E.g., blink LED exactly ten times
The following experiments use the same circuit we’ve been using (2 switches and 2 LEDs)

## Slide 21: We begin with the while loop
Example 0:
  var = 0; while(var < 200){ //These statements execute 200 times var++; //this is short hand for: var = var + 1; }

## Slide 22: Example 1: Count # Times Thru Loop
Arduino runs at 16 million instructions/second
This program counts the number of instructions executed while you hold down the pushbutton
Open the sketch: LoopCounter.ino and watch the monitor as you push the button

## Slide 23: Example 2: Measuring Time Duration
Measuring duration of an event is a common application
  E.g., how long has a button been pushed?
  Before proceeding, here are two useful facts:
Here’s a useful function: “millis()” gives # milliseconds since Arduino turned on
New variable type (use this when numbers get really big): “long int x;” or “long x;”
  “int x;” declares a 16 bit integer variable
    Handles values in the range: -32768 to +32767
  “long x;” declares a 32 bit integer variable
    Handles values in the range: -2.14 billion to +2.14 billion

## Slide 24: The Sketch
Modify your program to measure duration button is pushed (in milliseconds, or m.s.)
Complete sketch in LoopTimer.ino
Changes to make

## Slide 25
Objective: Work through Examples 1 and 2 to help you understand “while” statements
Look at the “for” statement, and work an example
Hands On

## Slide 26: Serial Monitor information
Arduino Serial.println sends data from Arduino to your computer where it is displayed on your monitor
  Uses Arduino pins 0 and 1 (“TX” and “RX”) for communication
    For this reason we advise: Never use pin 0 or pin 1 for Arduino projects
  Serial Monitor is a program that prints the values on your screen
Details:
  Serial.begin(9600) initializes communication rate at 9600 bps (bits per second)
  Serial.print: sends text or values to computer on same line
  Serial.println: same as print but also starts new print line
Hands On

## Slide 27: What do the numbers mean???
Upload LoopCounter.ino
What’s the smallest count you can get?
The number you see is how many times the computer executes the while loop as you held down the button
  Remember: Arduino does about 16 million operations each second
Hands On

## Slide 28: Very small values indicate switch bounce!
Problem affects most types of switches. It’s everywhere!
One button push!
One button push!
bounce
bounce
bounce
bounce
Hands On

## Slide 29: Software solution: sleep
Solution: make computer sleep for 20-40 ms after switch detected. This causes it to ignore bounces.
sleep
sleep
Hands On

## Slide 30: Debounce Your Program
Insert “delay(20);”
  Do values make sense now?
    void loop() {
    long int i = 0;
    while (digitalRead(switchPin) == HIGH){}
    delay(20); //wait for bounce to stop
    while (digitalRead(switchPin) == LOW) {
    i = i + 1;
    }
    Serial.println(i);
    delay(20); //wait for bounce to stop
    }
Bouncing occurs at front end and back end of button push
Hands On

## Slide 31: for statements e x t r e m e l y useful!
for (int x=0; x<100; x++) {
print(“x equals “);
println(x);
}
Declare x as an integer if it hasn’t been declared yet
Initialize x
The Test
Increment or decrement
Monitor output:
x equals 0
x equals 1
x equals 2
:
x equals 99

## Slide 32: Using a “for” statement
Repeat a task until condition met
for (int i=2; i<8; i++){
pinMode(i, OUTPUT); // “task”
}
Where ”i++” increments “i”
Equivalent to:
“for” loop flowchart
Initialize test increment
pinMode(2,OUTPUT);
pinMode(3,OUTPUT);
pinMode(4,OUTPUT);
pinMode(5,OUTPUT);
pinMode(6,OUTPUT);
pinMode(7,OUTPUT);
i=2
i
i<8?

## Slide 33: For-loop Practice
Open forExampleSkel.ino
Run it: how does it work?
Your Job: Add a second for-loop that blinks Right LED 10 times with a delay of 100 ms
Add Code Here
Hands On
Solution in forExample.ino
Notes: forExample.ino

## Slide 34: Analog Inputs
Analog-to-Digital Converters
Potentiometers (“Pots”)
Serial Plotter
Pulse Width Modulation (PWM)
RGB LED

## Slide 35: Questions
When people talk about “analog” What does that mean?
When people talk about “digital” What does that mean?

## Slide 36: Analog and Digital Signals
Digital signals are 0V (“LOW”) or +5V (“HIGH”)
Analog signals vary continuously between 0 and 5V
5V
0V
5V
0V
time
time
digital
analog
voltage
voltage
Where computers live
Where humans live
How can we communicate between these worlds?

## Slide 37: Analog-to-Digital Converter “ADC”
Analog voltage is measured at Arduino input pin
Converted to Digital value used in Arduino sketch
2-bit ADC
22 = 4 values
3-bit ADC
23 = 8 values
Zero
One
Ten
Eleven
0
1
2
3
4
5
6
7
binary
decimal
Some arbitrary analog signal like speech
binary
Quiz question: would you rather have 100 (binary) doughnuts or 6 (decimal) doughnuts?

## Slide 38: Analog Inputs
Arduino Uno has six ADC input pins
  A0, A1, A2, A3, A4, and A5
  These can also be used as digital input/outputs
Input voltages between 0 and 5 volts
ADC value is 10 bit integer
  There are 210 = 1024 possible integer values
  Values range from 0 to 1023

## Slide 39: Potentiometer (“Pot”)
We’ll use it to generate an analog signal
A water spigot varies the water pressure
A pot varies the voltage
Turn the knob and change the resistance to flow
Find yours in your kit…
Came in the big bag
Comes in the kit as two pieces
Not the best quality…
These are nice

## Slide 40
Potentiometer or “pot”
Wiper voltage
Resistive material
Wiper Output
Knob turns the Wiper
Wiper voltage depends on position of knob
  Voltage decreases as current flows through resistive material
  Therefore, wiper voltage controlled by knob rotation
Example: volume control in audio equipment
+5 V
0 V
“Wiper”

## Slide 41: This is called a “Voltage Divider” circuit
Voltage is “divided” into two parts
  Some is across R1, the rest is across R2
Provides a way us to control voltage
  Current enters R1 with voltage Vs
  It loses energy as it passes through R1
    Voltage drops from Vs to V2
  It loses the remainder of its energy passing through R2
    Voltage drops from V2 down to zero, also known as “Ground”
Result: R1 and R2 control the voltage V2
V2
Arduino
A0
GND
Battery or Arduino
current

## Slide 42
Objective: Understand analog inputs
  Voltage divider and potentiometer
  Serial Plotter (not available on Arduino Create)
  Pulse Width Modulation (PWM)
Hands On

## Slide 43: Get a Built-in Example
Click: File -> Examples -> Basics -> AnalogReadSerial
Hands On

## Slide 44: Experiment
Change to 100
How this C program works…
  First: change delay from 1 to 100 ms
    makes output slower and easier to read
Hands On

## Slide 45: Use the Metal Pot (if you have one)
Push in hard!
(don’t be gentle)
Hands On
Good Pot
(courtesy of UW!)

## Slide 46: Upload the Sketch
Turn on Serial Monitor.
Rotate the potentiometer
Confirm that values range between 0 and 1023
Hands On

## Slide 47: Serial Plotter
Exit from Serial Monitor (click the “X” button)
Start the Serial Plotter (tools
Turn the Potentiometer knob
Hands On

## Slide 48: What We Learned
Arduino can measure a voltage
  Possibly from a sensor like a photo-resistor
  Or from a potentiometer
The voltage reading is an integer between 0 and 1023
Now we can write an Arduino program that makes decisions based on the measured value in some intelligent way
Hands On

## Slide 49: Pulse Width Modulation (PWM)
Controlling the brightness of an LED or the speed of a motor using analogWrite()

## Slide 50: analogWrite(): It’s not Analog!
analogWrite(pinNo, value);
You would think that the output voltage is “value”
  But you’d be wrong
Outputs 5V or 0V to pinNo
  This is a digital signal
  Average voltage is determined by “value”

## Slide 51: PWM Controls Average Voltage
Average Voltage is:
Examples:
analogWrite(pinNo, 51);
analogWrite(pinNo,128);
analogWrite(pinNo, 204);

## Slide 52: PWM Restrictions
analogWrite(pin, value);
  Values outside this range give erratic results
PWM only on Pins: 3, 5, 6, 9, 10, and 11!
  Indicated by “~” (tildas)

## Slide 53: Try it
Connect LED + resistor to pin 9
Pot to pin A0
Use Built-in Example: Examples–>Analog->AnalogInOutSerial
Hands On
A0
9
Perceived brightness changes even though voltage is only 0 or 5V

## Slide 54
How it works
  Potentiometer: sensorValue is between 0 and 1023
  Map: converts value to a number between 0 and 255
  analogWrite: Outputs PWM signal to LED
PWM is also used to control the speed of dc motors
Hands On

## Slide 55: Using PWM with an RGB LED
What is an RGB LED?
  “LED” = Light Emitting Diode, “RGB” = Red, Green, Blue
  An RGB LED contains a red, green, and blue LED used to create different colors
  A RGB LED has four pins: one for ground and one for each color
  Can think of making colors in a RGB LED like mixing paint
    Different amounts of red, green, and blue paint can produce different colors. Use different amounts of red, green, and blue light to accomplish the same thing!

## Slide 56: What is an RGB LED?
A common way to represent colors is using the RGB triplet. The values can range from 0 to 255, with 255 being the maximum value. For example:
  Red = (255, 0, 0)
  Green = (0, 255, 0)
  Blue = (0, 0, 255)
  Purple = (255, 0, 255)
  White = (255, 255, 255)
We can also use PWM to vary the brightness, or amount of light, that gets used to create each color → different shades
  To keep it simple we will only use PWM to vary the brightness of the LED and not create different shades in this module

## Slide 57
Objective:
  Build simple circuit using the RGB LED
  Use PWM to cycle through various colors on the RGB LED
Hands On

## Slide 58: Build this Circuit
The longest pin on the RGB LED is the GND
Use the picture below to distinguish which pin controls with color
Hands On

## Slide 59: Your Assignment:
Open RGB_LED.ino from Templates folder
Edit it to increase and decrease the value on the Red LED
Does it do what you expected?
Hands On
void loop() {
// Write code that increases the red pin
// from 0 to max brightness then decreases
// it to 0. This will cause the LED to flash red
// increment/decrement by 5
for (outputValue = 0; outputValue < 256; outputValue +=5)
{
analogWrite(analogOutRed, outputValue);
delay(10);
}
for (outputValue = 255; outputValue >=0; outputValue -=5)
{
analogWrite(analogOutRed, outputValue);
delay(10);
}
}

## Slide 60: RGB LED code
Hands On
The block of code we created will cause the RGB LED to flash red on and off.
Now duplicate the code so that the RGB LED will also cycle through green and blue.
Challenge: add some more colors to the forever loop by changing which Color Pins are changed by PWM. You can view the full code in the completed code directory.
Hint: The color combinations that we can create are:
  Yellow → (255, 255, 0)
  Purple → (255, 0, 255)
  Teal → (0, 255, 255)
  White → (255, 255, 255)

## Slide 61: Practical Use of analogInput Make a Voltmeter and an Ohm meter
Converting ADC value (0 to 1023) into a physically meaningful number
Learning about Floating Point variables
Optional Projects if We Have Time

## Slide 62: Convert analogRead() to Volts
We know that: 0 ≤ analogRead ≤ 1023
Let’s Convert it to: 0 ≤ Voltage ≤ 5
Formula:
analogRead value
(we have this)
0
1023
Actual Voltage (volts)
(we want this)
0
5

## Slide 63: Voltmeter Sketch
Start with same circuit as before
Open the Built-In example program
Basics -> AnalogReadSerial
Save As new file: Voltmeter
  We’ll modify this program to be a Voltmeter

## Slide 64: “Floating Point” Variables
Integer variables will not store fractions
“Floating Point” variables store fractional values
Add the following lines to the end of loop()
  Place code just before the final right curly bracket
Converts integer sensorValue to floating point V
  float V = 5.0*sensorValue/1023.0;
  Serial.print(“Voltage: “);
  Serial.println(V); //print V and begin new line

## Slide 65
Objectives:
  Voltmeter Experiments
  Ohmmeter Experiments
  Final project: ohmmeter plus LED display
Hands On

## Slide 66: Experiment #1
Turn on Serial Monitor or Plotter
Measure voltage on pin A0 as you turn potentiometer
You should see values between 0 and 5 Volts
A0
Hands On

## Slide 67: Experiment 2: Floating Input
Recall: An unconnected pin is called a “floating input”
Unplug the wire to the pot
  The wire connected to A0 now hangs free in the air
  We say that A0 is “floating” (usually a BAD thing)
Activate Monitor (or Serial Plotter if you’re using Desktop IDE)
Move your finger on and off of the wire to A0
Random Noise!!!!
Result depends on your location
floating input
Hands On

## Slide 68: Experiment #3
Use your voltmeter to measure button battery
  Works on any battery as long as
Button Battery
Jumper
Pot
Not used
Jumper
Hands On

## Slide 69: Next Project: Build an Ohmmeter
Tired of identifying 220, 1K, and 10K ohm resistors?
  Wouldn’t it be nice if you could just measure the resistance?
Arduino cannot directly measure resistance
  Must use a voltage divider to convert resistance to voltage
Hands On

## Slide 70: Theory of Operation
V4
Rtest
Rref
Rref is Any known resistor
V4 is voltage measured on pin A4
  Any analog input would work: A0, A1, …, A5
Solve for unknown resistor Rtest.
Voltage divider equation:
Algebra gives:
Recall Voltmeter:
Combine and simplify:
Unknown resistor
Known resistor
Hands On

## Slide 71: Make a New Sketch: OhmMeter.ino
Save your Voltmeter sketch as a new sketch called OhmMeter
We’ll edit the sketch to convert it into an ohm-meter
Following slides contain the basic changes
Hands On

## Slide 72: Create the OhmMeter sketch
Enter the following C commands at the top:
Hands On

## Slide 73: OhmMeter.ino (cont’d)
Keep typing:
Hands On

## Slide 74: Your Job:
Build the circuit using Rref= 1000 Ohm
Upload the sketch
Open Serial Monitor
Test different resistors
  Test a 220, 1000, and 10,000 Ohm resistor
    How is the accuracy?
  Also measure resistance of a photo-resistor (in light and in shadow)
Hands On

## Slide 75: The Ohmmeter Circuit
Unknown
Resistor Rtest
Reference
Resistor
V4
Rtest
A4
Rref= 1000
Rref=1000
Hands On

## Slide 76: Final Project (if you have time): Ohmmeter + LED Display
Let’s add a visual display to our Ohmmeter
Three LEDs will display different resistors:
  Measure the unknown resistance Rtest
  If Ohms, Turn on Blue LED
  if Ohms, Turn on Yellow LED
  if Ohms, Turn on Red LED
  if Ohms, Blink the Red LED
Hands On

## Slide 77: The Modified Circuit
Rref=1000
Rref
Hands On

## Slide 78: Modifications to setup()
LEDs are connected to pins 2, 3, 4
  So you need to add pinMode statements to setup
  E.g., pinMode(2, OUTPUT);
  Additional pinMode statements are required for pins 3 and 4
You can access the following sketches
  OhmMeterPlusSKEL.ino (skeleton code)
Hands On

## Slide 79: Modifications to loop()
Hands On
Add this code

## Slide 80: Your Assignment
Understand the code
Open skeleton code: OhmMeterPlusSKEL.ino
Edit to make the changes shown above
Test circuit with:
  220 Ohm
  1K Ohm
  10K Ohm
  100K Ohm
  Photoresistor, in light and in shadow
Hands On