## Slide 1: Programming the Arduino
Arduino Program called a “Sketch”
Arduinos use the C++ language
(plus a few custom functions)

## Slide 2: Flow Chart for All Arduino Programs
void setup()
  Commands that happen once.
  Initializations
void loop()
  Commands that repeat forever
  Gets the work done
Start
void Setup() {
Initialize stuff
}
void Loop() {
Do stuff
}
Happens once at start-up
Repeats 16 MILLION Times each Second
Start here. (Power On, Upload or Reset)
Flow Chart for All Arduino Sketches

## Slide 3: Introducing…. The BLINK Sketch
Makes an LED blink on and off
What goes in the Setup() function?
What goes in the Loop() function?
Let’s find out

## Slide 4: void setup() Initialize Stuff
“setup()” is a “function”
  Statements can be grouped between curly brackets: {}
  Statements end with semi-colon: ;
  “void” means this function does not return a value
pinMode(13, OUTPUT);
  This sets pin 13 to be an output pin (e.g., outputs voltage to LED)
Matching curly brackets

## Slide 5: void loop() Does Stuff
digitalWrite(13,HIGH); //sets Pin 13 to +5V (turns on LED)
delay(1000); //waits 1000 ms, which is 1 sec
digitalWrite(13,LOW); //sets 13 to 0V (turns LED off)
delay(1000); //waits another second
Matching curly brackets
Time (milliseconds)
HIGH
LOW
0
1000
2000
3000
4000
Pin 13
…

## Slide 6: Meaning of: HIGH and LOW
LOW means 0 volts
HIGH means the maximum system voltage
  For Arduino, HIGH = +5V (= 3.3V for Raspberry Pi)
The following are all equivalent:
  HIGH same as true same as 1
  LOW same as false same as 0

## Slide 7
Objectives
  Write the Blink sketch
  Upload and experiment
Hands On

## Slide 8: Start Desktop Arduino
Arduino Desktop users:
Start the IDE by double clicking the Arduino desktop icon
Hands On

## Slide 9: Open a New Sketch
Click Here
Hands On

## Slide 10: Edit Sketch to look like this:
Hands On
;

## Slide 11: As you type: Be Careful! C++ is “Case Sensitive”
E.g., you must type: pinMode
  These won’t work: pinmode, PINMODE, etc
E.g., you must type: OUTPUT
  It won’t work if you type: output
Hands On

## Slide 12: Compile, Upload, and Run
Click Here
Hands On

## Slide 13: Circuit for BLINK
For this simple experiment, we’ll use the LED that comes pre-wired on every Arduino
LED plus current limiting resistor is connected to pin 13
  The LED turns on when we write HIGH to pin 13
  The LED turns off when we write LOW to pin 13
Hands On
Built in LED
Notes: From https://www.arduino.cc/en/Tutorial/Foundations/DigitalPins:
NOTE: Digital pin 13 is harder to use as a digital input than the other digital pins because it has an LED and resistor attached to it that's soldered to the board on most boards. If you enable its internal 20k pull-up resistor, it will hang at around 1.7V instead of the expected 5V because the onboard LED and series resistor pull the voltage level down, meaning it always returns LOW. If you must use pin 13 as a digital input, set its pinMode() to INPUT and use an external pull down resistor.

## Slide 14: Things To Try
Experiment with different on and off delays
  Click Upload after each change
E.g., what is smallest delay that can be seen?
  Consider the TV frame rate (“refresh rate”)
    Traditional TV uses 60 frames/sec (60 on + 60 off each sec)
    Time per frame = 1/60 = .0167 sec  17 milliseconds (ms)
  Try this: set blink rate = TV frame rate
    Try “on” time = 8 ms; “off” time = 9 ms (total = 17 ms)
  What rate causes visible flicker?
    Many modern TVs use 120 frames/sec – Try it!
Hands On

## Slide 15: Variables
Very important in programming languages!

## Slide 16: Annoying Problem
If we want to change any number (such as 13)
  We must change EVERY occurrence.
  Tedious and error-prone

## Slide 17: Solution: use “variables”
Modify your Blink sketch to look like this:
  Integer Variable “LEDpin” has been assigned value of 13
  Integer Variable “onTime” has been assigned value of 100
Try changing onTime and offTime and re-run it
“int” declares a variable to be an integer
variables must be declared once and only once
Optional comments

## Slide 18: Project: Cylon (Battlestar Galactica)
Parts: 4 LEDs, 4 resistors, jumpers, Arduino
Your Challenge:
  Build a Cylon circuit
  Modify the Blink Code to blink 4 LEDs

## Slide 19: Cylon Circuit
Pins 0 and 1 are rarely used

## Slide 20: Circuit Diagram
Questions
Q: What resistor to use?
Q: What color LEDs?
Q: LED long leg go on the left or right?

## Slide 21: Circuit Hint
Questions
Q: What resistor to use?
A: 220 Ohm
Q: What color LEDs?
A: your call!
Q: LED long leg on left or right?
A: Long leg on LEFT
220
220
220
220
red
green
blue
yellow
long
short
220

## Slide 22
Build the circuit, write the Sketch, get it working
If you have trouble with the sketch, a working version cylon.ino is available in the sketches folder
When you’re done, it’s lunch time!
Hands On

## Slide 23: Cylon “Pseudo Code”
Setup should include these statements:
pinMode(2,OUTPUT);
pinMode(3,OUTPUT);
pinMode(4,OUTPUT);
pinMode(5,OUTPUT);
Loop code should do this:
Blink 2 on and off
Blink 3 on and off
Blink 4 on and off
Blink 5 on and off
Blink 4 on and off
Blink 3 on and off
Note: this is not the actual code!
Suggestion:
Write code to blink LED on pin 2
Use copy-and-paste to replicate blink code for pins 3, 4, and 5.
Hands On

## Slide 24: First Few Lines of Cylon
Use Copy and Paste to fill out the remaining blinks. Then edit to use correct pin numbers.
Save As file: Cylon
Hands On

## Slide 25: Intro to Functions

## Slide 26: What Are Functions?
Example: digitalWrite(3, HIGH);
digitalWrite is not part of C++ language
It is just a small built-in program that does all the small tasks required to set pin 3 to 5V
  Nice because we don’t have to repeat all those commands each time we want to turn on an LED
It’s easy to write our own functions!

## Slide 27: Intro to Functions
Let’s write a function called blinkit(x);
Purpose: to blink the LED connected to pin x ON then OFF.
  Where x is integer variable
  x is called an “argument”

## Slide 28: The new Cylon program using blinkit
  void loop(){
  blinkit(2); //blink the LED on pin 2
  blinkit(3); //blink the LED on pin 3
  blinkit(4); //blink the LED on pin 4
  blinkit(5); //blink the LED on pin 5
  blinkit(4); //blink the LED on pin 4
  blinkit(3); //blink the LED on pin 3
  }
  It’s much nicer, isn’t it?

## Slide 29: The ‘blinkit’ function
  void blinkit(int x){
  // This function blinks the LED on pin x once
  digitalWrite(x,HIGH);
  delay(1000); //keep LED on for 1 sec
  digitalWrite(x,LOW);
  delay(500); //keep LED off for .5 sec
  }
Working version is “cylonfunc.ino”

## Slide 30: Here is the Complete Sketch
Some Rules:
The blinkit function must be OUTSIDE of other functions (not within their curly brackets)
Functions should occur before setup and loop
Hands On

## Slide 31: Try Out Different Blink Patterns
  void loop(){
  blinkit(2); //blink the LED on pin 2
  blinkit(4); //blink the LED on pin 4
  blinkit(3); //blink the LED on pin 3
  blinkit(5); //blink the LED on pin 5
  blinkit(5); //blink the LED on pin 5
  blinkit(3); //blink the LED on pin 3
  }
Now you can build a Christmas Tree Light System!!!
Hands On

## Slide 32: Challenges
Extend your Cylon project with these features:
Modify circuit to have 8 LEDs
Modify code to have an “Interesting” blink pattern
Modify blinkit to allow variable LED delays
  For example: blinkit(5, 100, 500); //LED pin 5, on 100, off 500
  Skeleton code is provided to help you in the CylonFuncPlusSkel folder
Hands On