## Slide 1: Welcome to Engineering Summer Program for Teachers 2025
ELECTRICAL ENGINEERING AND COMPUTER SCIENCE, COLLEGE OF ENGINEERING AND PHYSCIAL SCIENCES

## Slide 2: Getting Started
Go to desktop folder: Workshop Materials\Arduino\Day 1 - Arduino
Open this presentation: ElectronicsIntro.pptx or ElectronicsIntro.pdf
What to do
  Follow along. Go forward or backward at your own pace
  During Hands-On sessions you can
    Zoom in or Zoom out on detailed diagrams
    Go back to previous slides
    Work ahead if you want to

## Slide 3: Basic Electronics
Let’s get started!
ELECTRICAL ENGINEERING AND COMPUTER SCIENCE, COLLEGE OF ENGINEERING AND PHYSCIAL SCIENCES

## Slide 4: Find LED and Battery
LED
3V Battery
Extract from Remote Control
Any color of LED is ok

## Slide 5: Making LEDs work
Our First Circuit
Find the button battery
Find an LED
Touch battery to the LED legs – does LED light up?
Can we find a rule to make the LED light?
LED
3V Battery
Place long leg on (+) side
Short leg on the (-) side
Notes:   Connect long leg to + (anode)
  Connect flat side to – (cathode)

## Slide 6: How to Connect LED
LONG leg to PLUS
SHORT leg to NEG
Long Leg
Short Leg
Circuit Diagram
Notes:   Connect long leg to + (anode)
  Connect flat side to – (cathode)

## Slide 7: Current Flow
Electricity flow is called “current”
  It flows from plus+ to minus-
A “Diode” only lets current flow one way
LED is “Light Emitting Diode”
  Lights up only when current is flowing
+
-
Current
I>0
LED
Battery
Wire
Emits LIGHT
+
-
No current
I=0
Wire
Battery
Emits DARK
LED
Current
Blocked!
Notes:   Connect long leg to + (anode)
  Connect flat side to – (cathode)

## Slide 8: Interesting Details
Electrical engineers refer to current as “I”
  Current “Intensity”
A battery is called a “voltage source”
  Produces constant voltage, but current can vary
Batteries have plus(+) and minus(-) sides
  Alternative notation: plus(+) and Ground (GND)
    Think of Ground as being at zero volts
  E.g., the 5-volt Arduino power supply is labeled: "+5V” and “GND”

## Slide 9: Electricity: the Water Hose Analogy
Resistance
“Ohms”
Pressure
“Volts”
Current
“Amps”
Notes: Thumb on end of hose varies resistance. Which varies current.
Which makes a good water fight.
Voltage is a measure of available energy in each unit of charge.
It’s like how many gallons of gasoline are in your tank

## Slide 10
Here’s the math
Here’s what’s really happing

## Slide 11: Set Up Your Resistor bags
Your kit includes many resistor values.
Find the following: 220, 1K, 10K
  We’ll use these in this workshop
Good idea to put them in small plastic bags.
  Label them with a Sharpie
bag 1
bag 2
bag 3
220
Ohms
1K
Ohms
10K
Ohms

## Slide 12: Find Your Jumpers
Cut off
We use these to make electrical connections
Remove the binder from the jumpers
Notes about using jumpers:
  Color doesn’t matter
  Use the shortest jumper that works (for neatness)

## Slide 13: Making Connections
Permanent circuits are usually connected using “solder”.
For experimentation, we use “Solderless Breadboards”
Everyone please get your breadboard
Solder connection
No solder needed
Breadboard

## Slide 14: How They Work
Each group of 5 holes is connected electrically
Side “rail” holes are connected as well
Please Don’t Do This!
Front
Back
Side Rails

## Slide 15
How to connect power to a breadboard
  We’ll get voltage from Arduino, not from a battery
  Use jumper to connect 5V to any Red hole
  Use jumper to connect GND to any Blue hole
    Arduino has three GND sockets – whichever is convenient.
Optional: add jumpers from top to bottom
Good idea to keep them on all week
Now, both top and bottom rails can be used for +5V or GND
5V
GND
GND
GND
5V
GND

## Slide 16
RA
RB
RC
+5V
Example Circuit
RA
RB
RC
+5V
GND
+5V
GND
To Arduino GND and +5V
Symbol for GND

## Slide 17
RA
RB
RC
+5V
Showing Internal Connections
RA
RB
RC
+5V
GND
+5V
GND
To Arduino GND and +5V
Symbol for GND

## Slide 18: Build your first breadboard circuit
Schematic Diagram
(long)
(short)
First: try 220
Then: try 10k
short(-)
Guidelines:
Any wire colors work
Usually Red = 5V
Usually Black = GND
LED
Hands On
Notes: More resistance = less current = less light
Less resistance = more current = more light

## Slide 19: Build your first breadboard circuit
Schematic Diagram
(long)
(short)
First: try 220
Then: try 10k
short(-)
Guidelines:
Any wire colors work
Usually Red = 5V
Usually Black = GND
LED
Hands On
First: try 220
Then: try 10k
LED
Notes: More resistance = less current = less light
Less resistance = more current = more light

## Slide 20: Connect Arduino to computer using USB Cable
  Avoid USB Sockets on the monitor…
    The’re not always connected
USB Cable
Hands On
Notes: More resistance = less current = less light
Less resistance = more current = more light

## Slide 21: What Happened?
R=10K (10000 Ohm) resistor = Dim
R=220 Ohm resistor = Bright
Why? Ohm’s Law:
  More resistance  less current  less light
What if R is really small or use a jumper (R = 0)?
  Small R  Lots More current  much brighter LED
  Problem: Excessive current can damage the LED, and possibly even damage the Arduino
Hands On

## Slide 22: Takeaway Lesson
Always use a resistor to protect the Arduino and LEDs
  Called “current limiting resistor”
Resistance value is not critical, as long as it’s greater than 100 ohms
  We usually use 220 ohms because many are included in our kit
  Choose larger values for dimmer LED, e.g., 1K to 10K
The resistor can go on either the short leg or long leg side of the LED
Short Leg
Either works fine
Hands On

## Slide 23: Add pushbutton switch (and please put the resistor back in)
220
“Series” circuit
Pushbutton Switch
You may have to bend the legs a little
Pushbutton MUST be placed over gap
gap
Hands On

## Slide 24: Pushbutton Switch
Pushing the button temporarily connects the left two pins to the right two pins. Current can flow.
When button not pushed, it blocks current flow
Hands On

## Slide 25
Next, add a Photoresistor
Also called a “Light Dependent Resistor” (LDR) or “Light Sensitive Resistor” (LSR)
Photoresistor
220
LDR
Schematic Diagram
Hands On

## Slide 26
Move your finger over the photo resistor (while pushing the button)
Photo-Resistance increases as light decreases
More light (less resistance)
   More current
   Brighter LED
Hands On

## Slide 27
This is called a “Series Circuit”
Order of components doesn’t matter!
Same current through all components
SAME!
LDR
LDR
Hands On

## Slide 28
That could read the pushbutton switch
That could read the light sensor or other sensors
That could automatically turn on LEDs using built-in timer
That could control motors, sounds, and displays
We had a computer??

## Slide 29: Part 2: Arduino Basics
ELECTRICAL ENGINEERING AND COMPUTER SCIENCE, COLLEGE OF ENGINEERING AND PHYSCIAL SCIENCES

## Slide 30: Arduino is a “Microcontroller”
Microcontroller = small computer Sometimes called a microcomputer or microprocessor
What can we do with a microcomputer?
Connect input devices to sense the world
  Sensors: temperature, pressure, light, gyroscope, microphone, GPS
Connect output devices to control the world
  Motors, actuators
  Speakers to make sounds and music
  LEDs and LCDs to display information
Connect to the world
  Easy to add wi-fi, blue tooth, ethernet, and long-range radio capabilities
Secret Sauce: computer programs that we write!

## Slide 31: Atmega328 micro-controller The Brain
“Pins”
“Pins”
Microprocessor
Memory
Communications
Clocks and Timers
Analog to Digital Converter
Notes: Point out what pins are so the next slide makes sense!

## Slide 32: What are “Pins”??
“Pins” 0-13
Microcontroller Pins
Microcontroller pins are wired to sockets
We plug jumper wires into sockets to make our circuits
These sockets are called “pins”
Arduino sockets called “Pins”

## Slide 33: What’s on board
Atmega328 micro-controller.
  16 MHz (not GHz!)
  32 kB program memory
  2 kB RAM (NOT GB!)
  Comparable to computer running the Hubble Space Telescope
General Purpose Input/Output (GPIO) pins 0 - 13
GPIO+ (adds “analog”) A0-A5
Power and Ground
Reset: restarts the program
1
3
2
4
5
GPIO pins 0-13
A fruit fly has about 100,000 neurons.
An Arduino has about 100,000 logic gates…
Notes: Original Hubble computer (DF-224) 1.25 MHz, built by Rockwell
First service mission (1993), added 16 MHz 387 coprocessor
3d service mission (1999), 25 MHz 486
A fruit fly comes preprogrammed to fly.
Arduino’s program memory starts out empty – what can we program it to do?

## Slide 34: Arduino UNO versions
We use the UNO Revision 3 (R3), released in 2011
  A new R4 version was released in 2023
R3 and R4 are mostly compatible, but
  R4 is faster, has more memory, includes LED matrix and WiFi
  Pricing: R4 is about $27, R3 clones are $5-10

## Slide 35: Why We Use R3 rather than R4
Learning to program is the same on both systems
  Except for advanced applications such as WiFi
R3 is robust (doesn’t damage easily). And it’s cheaper!
  Many inexpensive R3 clones and educational kits are available
  Currently, no cheap R4 clones are available.
For special projects you might need something more
  Consider the full range of Arduino development boards, capabilities, and prices. Maybe even consider a Raspberry Pi!

## Slide 36
Arduino
No Operating System, runs only one program at a time, not very fast, limited memory
Six analog inputs
Great at simple repetitive tasks, many sensors, many outputs, good in “embedded systems”
Requires little electrical power
  Battery lasts a long time
Like R2-D2
Raspberry Pi
Linux, general purpose computer, multiple programs run simultaneously, fast, lots of memory
No analog inputs
Great for running sophisticated software, browsers, games, word processing. But it’s overkill for simple applications
Requires 10x more power
  Power source is usually not a battery
Like C-3PO
Scrappy
Speaks only Binary
Suave
British Accent
Speaks 6 million languages
Both systems have a HUGE “eco system” for support