## Slide 1: Projects
Weather Station
Ultrasonic Distance

## Slide 2: Objectives
Arduino is great for sensing the environment
Our weather station will do the following:
  Measure sunlight
    Measure light sensor resistance (analog sensor)
    Convert ohms to luminance (Lux)
  Measure temperature (digital sensor)
    Convert temperature C to F
  Measure % humidity (digital sensor)
  Output measurements to LCD Screen
Notes: Point out that we’ve already measured voltage and resistance as earlier projects

## Slide 3: We Begin with a Photo Resistor
Gives indication of light level by changing the resistance

## Slide 4: Sensors have Data Sheets
Find a Data Sheet for the device (Google)
  Usually include instructions and physical properties
Relationship between measurement and environment.
  Rough approximation:
Our Device
Resistance
Properties of several commercial devices
Notes: Slope=b=(log(y2)-log(y1))/(log(x2)-log(x1))
logy1=2, logy2=log(600000), logx1=4, logx2=-1
B=(5.78-2)/(-1-4)=-.756
Log(y)-log(y1)=b (log(x)-log(x1)
Or
Log(x)=log(x1)+(log(y)-log(y1))/b = 6.64-1.32 logR
Or with x=Lux and y=R
Log(Lux)=5-log(R)

## Slide 5
Lumen = intensity of perceived light

## Slide 6: Photo Resistor AKA: Light Dependent Resistor (LDR)
We need to measure resistance
  But Arduino can’t directly measure R
  Use “voltage divider” along with our Ohmmeter sketch
Voltage V0 depends on how much light is present
  More light = less resistance  V0 large
  Less light = more resistance  V0 small
V0
Rref
RLDR

## Slide 7: Code Snippet for Light Measurement
void loop() {
rawLight = analogRead(lightPin);
//convert raw analogin reading to resistance
Rldr = Rref * (1023.0 - rawLight) / rawLight;
//convert resistance to approximate Lux
Lux = pow(10.0, 6.64 - 1.32 * log10(Rldr));
}
Read about pow and log10 at http://www.cplusplus.com/reference/cmath/”

## Slide 8: Advice
This Circuit is similar to OhmMeter
  Unknown resistance is photoresistor
  And now we use a 10K rather than 1K reference resistor
    Better accuracy if ref resistor similar in size to unknown resistor.
Modify OhmMeter sketch and save it as WeatherStation

## Slide 9: Sketch should look like this: (start typing)
(Answers folder: LightSensor.ino)

## Slide 10: Build this: Light Sensor Circuit
10 k
220
Leave room for future development

## Slide 11: Try It!
Upload the code
Turn on Serial Monitor
  Make sure it’s set to 9600 baud
  Make a shadow over sensor
Turn off Serial Monitor
Turn on Serial Plotter
  Tools -> Serial Plotter
Make sure this matches value in your code: Serial.begin(9600)
Serial Plotter
Time (samples)
Light Intensity (Lux)

## Slide 12: Using LCD: System Engineering
We may not know exactly how LCD works
We may not know exactly how Arduino works
But we know their interfaces
We can pull together many subsystems into a powerful complex system
How? Use Provided Examples!
File->Examples->LiquidCrystal

## Slide 13: Modify the Program
These declarations are added:
#include <LiquidCrystal.h> //use the LCD library
LiquidCrystal lcd(7, 8, 9, 10, 11, 12); //define the Pin connections
Added to setup():
lcd.begin(16, 2); //our LCD has 16 columns and 2 rows.
Added to loop():
lcd.setCursor(0, 0);
lcd.print("Light(Lux) "); //initialize 16 characters
lcd.setCursor(11, 0);
lcd.print(Lux);}
Note:
These special functions are defined in the LiquidCrystal library
It’s easy to see what they do
They are easy to use
But details are beyond our scope
In Answers folder: LightSensorLCD.ino

## Slide 14: Now (carefully) Add an LCD
Potentiometer
(Screen Contrast)
Wire Carefully!

## Slide 15: Temperature and Humidity
Find your DHT11 sensor
Has “embedded microprocessor”
  Sends temp and humidity data serially as 0’s and 1’s over DATA pin
  A Library is used to get the data
GND
VCC
DATA
Specifications:
Temp: 0-50 C
(32-122 F)
Humidity: 20-90%
Response: 2 sec
(it’s slow)

## Slide 16: Add in the DHT11 sensor
Add These

## Slide 17: DHT Library
You probably need to add the library: Sketch -> Include Library -> Manage Libraries…
  It may already be installed on your system
In Library Manager: Filter Your Search
  Type in: DHT
  Select: SimpleDHT
  Click: Install

## Slide 18: Upload: “LightSensorLCD_DHT11.ino” (in Answers folder)
Additions made for the DHT11:
byte temperature = 0;
byte humidity = 0;
byte data[40] = {0};
if (dht11.read(pinDHT11, &temperature, &humidity, data)) {
Serial.println("Read DHT11 failed");
return;
}
int tempc = (int) temperature; //convert from byte to int
float tempf= temperature*1.8+32.0; //convert to deg F
int humid = (int) humidity; //convert from byte to int
This is a bit beyond our scope
Advice: Use this example as template for your own code
Example taken from our Elegoo tutorial CD

## Slide 19: HC-SR04 Ultrasonic Distance Sensor
The Arduino Way!

## Slide 20: What’s Inside?
Lots! Good example of “Embedded System”
  Transducers, amplifiers, filters, and..
  Dedicated Microcontroller!
microcontroller
Systems within systems…
Notes: uP handles comm with Arduino, generates transmit pulse, signal processes return pulse, handles echo pulse

## Slide 21: Distance Sensor HC-SR04 Review
Range: 2 cm to 400 cm
Operates like this:
  Arduino makes Trig pin go HIGH then LOW
  HC-SR04 transmits 8 sound pulses at a rate of 40000 pulses per second (“ultrasonic”)
  HC-SR04 makes Echo pin go HIGH until reflection detected, then pin goes LOW.
Transmitter
Receiver
Trig
Pin
T2way
Echo
Pin
Trig
Echo
Ping
Transmitted
Echo
Received

## Slide 22: Timing Diagram
2-way travel time
Echo Detected
Arduino pin connects to HC-SR04 Trig pin
HC-SR04 sonic output
HC-SR04 makes Echo pin HIGH, then LOW when echo detected
HIGH
LOW
HIGH
LOW
HIGH
LOW
10 s
8 sonic pulses

## Slide 23: Sound Velocity and Distance
Total distance traveled by sound = 2D
“Two-Way” Travel time T2way = 2D/V seconds
Sound velocity V  34.3 (cm/ms) at sea level
  Or, V  .0343 cm/us
Distance to Target: D = T2wayV/2 meters
target
Distance D
Receive
Transmit
HC-SR04

## Slide 24: Using the Distance Sensor
The beam is narrow!
About
The target can’t be tilted!
Soft targets – not so good
target
Receive
Transmit
HC-SR04
Little reflection
“Min” surface = .5 m2

## Slide 25: Code Walkthrough DistSensSkel.ino

## Slide 26: Initiate a Ping
Trig
Pin
T2way
Echo
Pin
This causes HC-SR04 to send a PING
HC-SR04 sets “Echo” pin HIGH until return is detected
Echo Detected
Ping
Transmitted

## Slide 27: Wait for Echo
Here, we wait until echoPin goes LOW
Which indicates echo has been received
T2way
Echo
Pin
t0
Echo
Detected
Ping
Transmitted

## Slide 28: Compute Distance
Echo
Pin
duration=micros()-t0
t0
Plot distance data using Serial Plotter

## Slide 29: Make Your Circuit
pin 4 to “Echo”
pin 5 to “Trig”
Complete DistSensSkel.ino and upload it
Echo
Trig

## Slide 30: Challenge! Make a Distance Alarm
Modify circuit:
  Add one red LED plus 220 ohm resistor
Modify code:
  Add “if” statement: if distance is less than 20 cm, turn on red LED, otherwise turn it off
  Add a buzzer to the alarm